## Slide 1: MCTE 3104 Mechatronics Interfacing Lab
Session no. 10 : Introduction to IOT (Part II)

## Slide 2: Outline
HTTP (Hypertext Transfer Protocol) (review)
  Http and how the web works
  HTTP Methods
  REST API
ESP-8266
  Getting started with ESP-01 module
  Do http request
  Connect to Firebase Real-time database

## Slide 3
HTTP protocol
HyperText Transfer Protocol
One of the most widely used internet protocol in the world.
HTTP is an application layer protocol that allows web-based applications to communicate and exchange data
Think the HTTP as the messenger of the web
It is a TCP/IP based protocol
It is used to deliver contents, for example, images, videos, audios, documents, etc.
The computers that communicate via the HTTP must speak the http protocol
HTTP exist here!

## Slide 4
The Request-Response Cycle
file
file
file
file
client
server
Say a user wants to see a website and types in a url of the page usually on a browser.
The user needs to be physically connected to the internet; this is where the TCP/IP protocol makes communication on physical connection between machines possible.
When the connection is established, the client sends a request called HTTP message and then disconnects from the server waiting for a response.
The server on the other hand prepares the response, establishes the connection again and send back the response called HTTP message to the client and then disconnects.

## Slide 5
ESP8266

## Slide 6
ESP8266
Low cost microcontroller with full TCP/IP stack Wi-Fi capability produced by shanghai-based manufacturer Espressif Systems.
To use the ESP8266 a lot of modules are made for us to use
NodeMCU

## Slide 7
Esp8266 specifications
. 11 b/g/n protocol
. Wi-Fi Direct (P2P), soft-AP
. Integrated TCP/IP protocol stack
. Built-in low-power 32-bit CPU
. SDIO 2.0, SPI, UART

## Slide 8
ESP8266
So what are the few things we can do with this module?
. Create a web server
. Send HTTP requests
. Control outputs
. Read inputs and interrupts
. Send emails
. Post tweets
and many more…

## Slide 9
ESP8266
ESP8266 is Arduino code compatible which means you can write and code with using the Arduino IDE.
The ESP01 however does not have a USB-UART converter to communicate with the PC. So we have to use a separate USB-UART converter to flash codes in the ESP01.
Here are some cheap USB-UART converter you can buy online:
CH340G
FTDI - FT232RL
Prolific - PL2303

## Slide 10
USB – UART Converter
ATMEGA16U2
CH340G
FTDI - FT232RL

## Slide 11
ESP8266
Getting Started with ESP-01
1. We first need to install the ESP8266 Board in the Arduino IDE
. Open the preferences window from the Arduino IDE. Go to File > Preferences
. Enter http://arduino.esp8266.com/stable/package_esp8266com_index.json into the “Additional Board Manager URLs” field as shown in the figure below. Then, click the “OK” button.

## Slide 12
ESP8266
2. Install the ESP8266 boards
Search for Esp8266
Click install

## Slide 13
ESP8266
3. Select board as ‘Generic ESP8266 Module’
Now you can start uploading code to the ESP01

## Slide 14
ESP8266
Prepare the ESP01 for flashing codes (using UART-USB converter)
Connection:
ESP01 UART-USB
GND GND
VCC (3.3V) VCC (3.3V)
TX RX
RX TX
CH_PD VCC (3.3V)
GPIO1 GND
Note: if you’re using the Arduino board as a UART-USB converter, connect the TX of ESP01 to TX of Arduino board and connect the RX of ESP01 to RX of Arduino board.

## Slide 15
ESP8266
Prepare the ESP01 for flashing codes (using Arduino board as UART-USB converter)
Connection:
ESP01 UART-USB
GND GND
VCC (3.3V) VCC (3.3V)
TX RX
RX TX
CH_PD VCC (3.3V)
GPIO1 GND
Note: if you’re using the Arduino board as a UART-USB converter, connect the TX of ESP01 to TX of Arduino board and connect the RX of ESP01 to RX of Arduino board.
Note: by grounding the reset pin you disabled the main microcontroller (i.e. Atmega328 or Atmega2560). The Arduino board functions as a UART-USB converter.

## Slide 16
ESP8266
Now upload a test code to the ESP-01 to see if all connections are correct
If this orange message appears, it means you’ve successfully uploaded your code to the ESP-01
Try uploading the example blink code, or any empty code.

## Slide 17
The ESP8266HTTPClient library allows you to do http request to REST api.
Example 1: Making simple GET requests on the ESP8266
ESP8266 – Do http request
Output from the ESP8266

## Slide 18
Lab activity 1:
Find a free online REST API service and make GET requests using the ESP-01.
Http request a REST Api on the ESP8266

## Slide 19
. To connect to firebase, we can’t just use simple http request because Firebase requires a secure https request to be made.
. So we need to use Firebase library for the ESP8266 to connect to firebase we first need to install ArduinoJson library
ESP8266 Connecting to Firebase
. Go to https://github.com/FirebaseExtended/firebase-arduino and click ‘Download ZIP’
. Extract the file and put the folder in ‘…/Documents/Arduino/Libraries’ of your PC

## Slide 20
Example 2: Connecting to Firebase database using ESP8266
ESP8266 Connecting to Firebase

## Slide 21
Example 3: Connecting to Firebase database using HTTP Shortcuts
ESP8266 Connecting to Firebase
https://play.google.com/store/apps/details?id=ch.rmy.android.http_shortcuts&hl=en
Download HTTP Shortcuts app on your Android
curl https://my-iot-room.firebaseio.com/electrical-appliances/lights.json -X PUT -m 10000 -d {{toggleKey}}
. Add cURL command by following the same format below
Home page
Create variable

## Slide 22
Example 3: Connecting to Firebase database using HTTP Shortcuts
ESP8266 Connecting to Firebase
Since our variable is a toggle switch, everytime you press it will either toggle to value ‘1’ or value ‘0’. Feel free to explore other variables.

## Slide 23
Lab activity 2:
Using the ESP-01, control an led using the ‘HTTP shortcuts’ app. (make use of firebase)
ESP8266 Connecting to Firebase